## Slide 1: PID Control
NNFL 2019-20
Saksham Consul

## Slide 2: Overview
What is PID?
Importance
Motivation
Basic Theory
Implementation

## Slide 3: PID
PID Control stands for “Proportional Integral Derivative” Control
Used extensively in control engineering and automation
PID Controller
Sensor
Plant
+
-
Reference
Output
Feedback
Error

## Slide 4: Importance
Used Extensively in industry
Automation – cruising mode in vehicles!
Robotics

## Slide 5: Motivation

## Slide 6: Basic Theory
Controller Output = Response to current error + Response to history of error + Response to future (likely) error
This is just a differential equation!

## Slide 7: Laplacian operation from Mathematics III
A differential equation can be converted to an algebraic expression using Laplacian operator!
The plant describes the dynamics of the system, this to can be modelled as a differential equation too

## Slide 8: Hold On!
Derivatives and integrals are continuous in nature!
Modern computation is digital in nature! (Digital thieves in the analog world)
Solution: Discretization
Integration == Summation over small rectangles
Differentiaton == Difference of values at two time intervals divided by time interval

## Slide 9: PID Tuning
Tuning of PID controllers is done using various parameters like:
  Peak Overshoot
  Rise Time
  Setting Time
  Steady State Error
CL Response | Rise Time | Overshoot | Settling Time | SSE
 | Decrease | Increase | Small change | Decrease
 | Decrease | Increase | Increase | Decrease
 | Small change | Decrease | Decrease | No change
CL Response | Rise Time | Overshoot | Settling Time | SSE
 | Decrease | Increase | Small change | Decrease
 | Decrease | Increase | Increase | Decrease
 | Small change | Decrease | Decrease | No change

## Slide 10: NNFL Remix
Classically PIDs have been tuned using analytical ways like Direct synthesis, Internal Model or heuristic techniques like ZN Tuning, Tyres-Luyben tuning
Note: Heuristic is a fancy way of saying ‘jugaad’
Often than not, require domain expertise and painstaking experimentations.
Also static values do not allow proper working in different conditions!

## Slide 11
How about tuning using Neural Networks and Fuzzy Logic?
Known:
  Reference (input)
  Ideal Output (target)
Supervised learning? Fitness Function (GA optimization)
Let’s make things fuzzy?

## Slide 12: Coding Time!